## Slide 1
A Grammar-Enabled Generative Design Framework for Design Exploration of Deoxyribonucleic Acid (DNA) Nanostructures
A.J. Vetturini avetturi@andrew.cmu.edu
Professor Jonathan Cagan cagan@cmu.edu
Professor Rebecca E. Taylor bex@andrew.cmu.edu
Notes: Main title: 40 pt. Arial
Presenter Name: 16 pt. Arial
Presenters Title: 16 pt. Arial Italic

## Slide 2: Generative design has seen broad application in a variety of domains
Introduction
Methodology
Results
Conclusions
Q&A
Truss design through stochastic optimization1 and data-driven learning2
Images from https://help.autodesk.com/view/fusion360/ENU/?guid=GD-TUT-GE-BRACKET-QS
Generative design solutions that can produce many unique design solutions based on designer requirements
Target a specific part weight
Minimize total weight
1. Reddy and Cagan. Journal of Mechanical Design 117, no. 2A (1995): 315–21.
2. Zheng et al. Nature Communications 14, no. 1 (2023): 7563.
Notes: Generative design methodologies have rapidly advanced throughout literature and has been applied to fields such as topology design, architecture, trusses, etc. using a variety of methods (deterministic, analytical solutions to drive optimization compared to deep learning models).
Most interestingly, these solutions can also vary based on the input: ranging from an initial “guess” solution to deriving a full design solution from a minimal set of input conditions
Benefits of Deterministic: A truly optimal solution guided by pure mechanics / mathematics
Benefits of stochastic: Exploration, produce novel solutions to inspire ideation
Study on the left targeted a specific weight, the one on the right just minimized the total weight of the part.

## Slide 3: DNA origami nanostructures are an interesting design space with broad applications
Introduction
Methodology
Results
Conclusions
Q&A
Programmable design features to modulate immune pathway activation for therapeutics1
1. Du et al. ACS Nano 16, no. 12 (2022): 20340–52.
2. Tian et al. Nature Materials 19, no. 7 (2020): 789–96.
Example 1
DNA origami
Nanoparticle
Nanoscale synthesis of targeted material fabrication2
Example 2
A deeper review of DNA origami applications can be found at: Dey et al. “DNA Origami.” Nature Reviews Methods Primers 1, no. 1 (2021): 1–24.
Notes: One particularly mortivating design space is that of DNA origami nanostrures which …
DNA origami nanostructures are on the scale of ~10s to 100s of nanometers and can be used in a variety of applications.

## Slide 4: Generative approaches have considered the scaffold routing design of DNA origami
Introduction
Methodology
Results
Conclusions
Q&A
Two limitations:
The solution resembles the input mesh
Designer has limited control over the search
Designer Input
Input consists of:
Mesh
Optimizer hyperparameters
Objective function selection
Generated solution
1. Babatunde et al. Applied Sciences 11, no. 7 (021): 2950.
2. Babatunde et al. Journal of Mechanical Design 146, no. 051708 (2024).
Notes: The application is to either fill the mesh or coat the mesh which has applications in nanocasting methodologies.
“This solution requires that the designer fully consider and design their ideal mesh prior to the generative solution”. Relies on the expertise of the designer to create said mesh.

## Slide 5: Generative design offers an approach to searching a difficult space
1. Cagan and Mitchell. Environment and Planning B: Planning and Design 20, no. 1 (1993): 5–12.
2. Shea and Cagan. AI EDAM 11, no. 5 (1997): 379–94.
Challenges presented by DNA origami design:
Conceptual difficulty
Design software limitations
Lack of data
Computational cost of molecular dynamics simulations
Introduction
Methodology
Results
Conclusions
Q&A
Difficult design space to manually explore
3. Stiny, G. Environment and Planning B: Planning and Design 7, no. 3 (1980): 343–51.
4. Kirkpatrick et al. Science 220, no. 4598 (1983): 671–80.
Pros and Cons to Shape Annealing
Ability to encode design-specific context
Capable of searching complex spaces
Stochastic optimization enacts design exploration
Inherent bias by grammar rules
A solution to these problems is Shape Annealing1,2
Shape annealing is the combination of shape grammars3 with simulated annealing4
Initial state
Shape grammars
Notes: To talk a little more about the DNA origami design space…
One way to explore upon a difficult design space is through shape annealing which …

## Slide 6: The design space used in this problem is comprised of preserved regions and excluded regions
Introduction
Methodology
Results
Conclusions
Q&A
1. User input
2. Convert input to graph
3. Initialize first state
DNA origami frame hosting a gold nanoparticle1
Preserved regions Edges or vertices that remain in the final design
Excluded regions Regions where material can not be placed
1. Tian et al. Nature Materials 19, no. 7 (2020): 789–96.
DNA origami
Notes: To begin formalizing the design problem, I want to introduce some design elements I use in this work.
If > 6 mins, SPEED UP

## Slide 7: A graph grammar is used to modify a graph representing a polyhedral mesh
Introduction
Methodology
Results
Conclusions
Q&A
Graph Representation
Grammar Rules
Example design evolution
Example 3D mesh
Graph describing example mesh
(x, y, z)
Attributes
Terminal?
Edge length
Mesh visualized via ParaView (Ahrens et al. The Visualization Handbook 717 (2005): 50038–1.)
DNA designs visualized via VMD (Humphrey et al. Journal of Molecular Graphics 14 (1996): 33–38.)

## Slide 8: Simulated annealing1 is used to search the resulting space
Introduction
Methodology
Results
Conclusions
Q&A
Objective
Function
x
1
2
3
4
5
6
5
1. Kirkpatrick et al. Science 220, no. 4598 (1983): 671–80.
2. Huang et al. In Proc. IEEE Int. Conf. on CAD (ICCAD 86), 1986.
An annealing schedule2 varies T hyperparameter that balances exploration vs exploitation

## Slide 9: Designer can tune the constraints and objective of the problem
Introduction
Methodology
Results
Conclusions
Q&A
The objective and constraints of the problem can be defined using the (documented!) Python package1
1. https://github.com/CMU-Integrated-Design-Innovation-Group/Mango
2. Du et al. ACS Nano 16, no. 12 (2022): 20340–52.
Designer-defined constraint
Designer-defined objective
Repulsion constraint
for all pairs of 2 edges
 This handles cases of disconnected pairs
The backbone of DNA is negatively charged
Design objective
A design with as many edges in a volumetric box
min
Having more edges allows for a greater number of modifications2
Notes: Due to the variety of applications, it is often the case that a designer would want to specify various constraints and objectives to search for DNA origami designs

## Slide 10: Generative design offers the ability to tune the search space
Introduction
Methodology
Results
Conclusions
Q&A
Custom Objective
Additional Constraints
d
Input
Iteration #
Export design
Notes: An optimally directed solution

## Slide 11: The scaffold length must be fully considered in the search
Introduction
Methodology
Results
Conclusions
Q&A
DNA origami1 consists of:
Scaffold (~7k nucleotides)
Short, synthetic staples (20-60 nucleotides)
And when combined with a thermal annealing process, DNA origami nanostructures can be formed1!
This value can not be exceeded
Further, the design should ideally utilize as much of the scaffold as possible
1. Rothemund, P. Nature 440, no. 7082 (2006): 297–302.
Custom Objective
This custom objective will drive the search to use as much of the scaffold as possible
The scaffold length serves as an upper-limit constraint to the generative search

## Slide 12: Generative design can also be used to explore upon the design space
Introduction
Methodology
Results
Conclusions
Q&A
1. Shea and Cagan. AI EDAM 11, no. 5 (1997): 379–94.
2. Chen et al. ACS Applied Materials & Interfaces 10, no. 29 (2018): 24344–48.
Initial state
Shape grammars
Sometimes, generative design is used in an exploratory fashion, such as when the standard deviation is used as an aesthetic score1
Furthermore, recent approaches have proposed novel scaffolds of different lengths2
Variation in Edge Length
(Std. dev of normalized edge lengths)
Scaffold Length
?
Unexplored
space
Selected designs from Veneziano et al. Science 352, no. 6293 (2016): 1534–1534.
Notes: Dataset was meticulously designs (edges are all exact multiple edge lengths0

## Slide 13: Multiobjective optimization is well-suited for design exploration!
Introduction
Methodology
Results
Conclusions
Q&A
New grammar rules to expand / shorten a, b, c, 𝛾
Values are constrained on range: 25 < a, b, c < 120
Custom Objectives
Designer
input
d
0.2
0
0.1
20
10
40 nm
i.
ii.
iii.
iv.
i.
ii.
iii.
iv.
1. Suppapitnarm et al. Engineering Optimization 33, no. 1 (November 1, 2000): 59–85.
Additional Constraints
+ Multiobjective shape annealing1

## Slide 14: Combined with coarse-grain molecular dynamics1 simulations, new design features can be studied
Introduction
Methodology
Results
Conclusions
Q&A
1. Coarse grain molecular dynamics simulations performed using oxDNA (Poppleton et al. Journal of Open Source Software 8, no. 81 (2023): 4693.)
GPU acceleration provided by Rovigatti et al. Journal of Computational Chemistry 36, no. 1 (2015): 1–8.
With generative design tools often producing non-obvious solutions, it is often the case where simulation results are desired by the designer to validate the solution
Max gap
Size (nm)
Images from https://help.autodesk.com/view/fusion360/ENU/?guid=GD-TUT-GE-BRACKET-QS

## Slide 15: Conclusions
Introduces a design framework capable of generating novel designs within a heavily constrained design space from a minimal set of input conditions
Establishes a design tool which does not require expert-level DNA origami design expertise and allows for design exploration of nanostructures in a side-by-side environment
Does not require a designer to fully conceptualize a solution a priori
Introduction
Methodology
Results
Conclusions
Q&A
Vetturini et al. In revision (2024).
No input design required by designer
Outputs many designs that a designer can observe choose from

## Slide 16: Thank you!
Advisors
Professor Jonathan Cagan
Professor Rebecca E. Taylor
My fellow researchers!
Integrated Design Innovation Group
Microsystems and Mechanobiology Lab
This work is supported by the NSF Grant Award CMMI-2113301
Introduction
Methodology
Results
Conclusions
Q&A
See more of my work @ ajvetturini.github.io

## Slide 17
Questions?
Introduction
Methodology
Results
Conclusions
Q&A
See more of my work @ ajvetturini.github.io

## Slide 18: Structural DNA nanotechnology leverages the properties of DNA to create nanostructures
Introduction
Methodology
Results
Conclusions
Q&A
https://www.britannica.com/science/DNA
Cytosine
Guanine
Adenine
Thymine
Watson-Crick-Franklin base pairs
1. Seeman, N. (1986). “Nucleic Acid Junctions and Lattices.” Journal of Theoretical Biology, 99 (2) 237-247.
DNA, the polymer
Phosphate
backbone
Nucleotides
Nano
particle
DNA, the structural material
Nucleic acid junctions1 allow for the design of nanometer-scale nanostructures
Junction
DNA
x
Notes: Before I can discuss design automation, I want to quickly discuss how DNA is used as a structural building material

## Slide 19: DNA origami is a manufacturing methodology enabling high experimental yield
Introduction
Methodology
Results
Conclusions
Q&A
1. Rothemund, “Folding DNA to Create Nanoscale Shapes and Patterns.”
100 nm
2D DNA origami nanostructures1
…
…
DNA Origami consists of:
Scaffold (~7k nucleotides)
Short, synthetic staples (20-60 nucleotides)
And when combined with a thermal annealing process, DNA origami nanostructures can be formed!
…
…
1.
2.
https://www.britannica.com/science/DNA

## Slide 20
1. Cagan and Mitchell. Environment and Planning B: Planning and Design 20, no. 1 (1993): 5–12.
Random walk of N steps
Reset initial state sn=1 and initialize T
Randomly apply rule to sn to create sn+1
Design constraints met?
Iterate success count
Replace active state sn with sn+1
No
Yes
Passed
Limit reached?
Iterate accept loop count
Failed
No
Yes
Equilibrium?
End!
Yes
No
Anneal T via annealing schedule
No
Iterate epoch count
Accept sn+1?
Do probability test
Yes
Shape annealing algorithm1

## Slide 21
1. Suppapitnarm et al. Engineering Optimization 33, no. 1 (November 1, 2000): 59–85.
Random walk of N steps with archiving
Return to base for state sn=1 and initialize all Tk
Randomly apply rule to sn to create sn+1
Design constraints met?
Iterate inner loop count
Replace active state sn with sn+1
No
Yes
Passed
Return to base?
Reassign sn and reset return-to-base count
Iterate accept loop count
Failed
No
Yes
Anneal Tk’s?
End Search?
End!
No
Yes
Iterate return-to-base count
Anneal all Tk and reset related counters
Yes
Iterate epoch loop count
No
Iterate return-to-base count
Iterate inner loop count
Archive s2?
Do probability test
Yes
Multiobjective shape annealing algorithm1

## Slide 22: Automated design software enables rapid sequencing of polyhedral nanostructures
Wireframe DNA origami
Greater specificity in 3D space due to design automation
Often seen as material-efficient
Introduction
Methodology
Results
Conclusions
Q&A
Design automation pipeline
Automated
Software1,2,3
Standard 3D mesh
ATTCG...
CGTAC…
GCTTA…
…
Scaffold
Staple 1
Staple N
…
DNA origami
AFM1
Cryo-EM1
Scale bar: 20 nm
Lattice based designs have larger cross sections4
1: Veneziano et al., “Designer Nanoscale DNA Assemblies Programmed from the Top Down.”
2: Benson et al., “DNA Rendering of Polyhedral Meshes at the Nanoscale.”
3: Jun et al., “Rapid Prototyping of Arbitrary 2D and 3D Wireframe DNA Origami.”
4: Castro et al., “A Primer to Scaffolded DNA Origami.”
a. Input
b. Select automated software
c. Software produces required sequences
d. Manufacture and characterize
Notes: REMINDER: You have a scaffold length constraint (a maximum amount of building material)

## Slide 23: The HRSV1 cooling schedule uses the epoch-to-epoch objective function valuations to determine the change in temperature
Te: Temperature at epoch e
: Standard deviation of objective function values at epoch e
1. Huang et al. In Proc. IEEE Int. Conf. on CAD (ICCAD 86), 1986.

## Slide 24: The various design constraints of this design space

## Slide 25: Lattice-based compared to wireframe DNA origami
1. Dey et al., “DNA Origami.”
2. Rothemund, P.W.K. Folding DNA to Create Nanoscale Shapes and Patterns. Nature 2006, 440, 297–302
3. Jun et al., “Rapid Prototyping of Arbitrary 2D and 3D Wireframe DNA Origami.”
4. Poppleton et al., “Design, Optimization and Analysis of Large DNA and RNA Nanostructures through Interactive Visualization, Editing and Molecular Simulation.”
How DNA Origami is manufactured1
Sample 2D DNA Origami2
Lattice Based
Higher structural rigidity
More material expensive
Generated via ATHENA3
Visualized in oxView4
Wireframe
Ease of designing in 3D
Less material expensive
Structural rigidity varies
Scaffold
Staples
Image created with BioRender.com.
Notes: 1:45
"DNA Origami is a class of DNA Nanostructures where a long scaffold strand is folded into an arbitrary shape through the use of staple strands"
Finite length of scaffold which has defined how we design the structures which lead to these two classes
Mention that the automated routing doesn’t check for strand length so that is based on the designer
Mention what DAEDALUS is for routing DNA in this model
Strength to weight ratio

## Slide 26: However, exploring upon the design space for wireframe topologies is difficult
While the design automation greatly reduces the design difficulty, there are still difficulties related to the automated design software motifs
Introduction
Methodology
Results
Conclusions
Q&A
DNA Origami consists of:
Scaffold (~7k nucleotides)
Short, synthetic staples (20-60 nucleotides)
And when combined with a thermal annealing process, DNA origami nanostructures can be formed!
1
1
1
Scale design
42
42
42
1
1
1
Scale design
48
48
42
48
This value can not be exceeded
Difficult to track!
as well the scaffold
length constraint